Embargoed: Not to be published before 07.00 CET 27 September 2012

Significant improvements for upgraded Sorento

- Fresh new look with premium appeal for popular Sorento SUV

- New 2.4-litre GDI gasoline engine generates 192 ps

- Stronger bodyshell improves ride, handling and refinement

- High-tech active safety technology enhances protection

Frankfurt, 27 September 2012 – The upgraded Kia Sorento SUV incorporates significant changes, including a re-engineered bodyshell, a new 2.4-litre GDI engine among a range of enhanced powertrains for better fuel economy with lower emissions, improved ride, handling and refinement, additional high-tech convenience and safety features, plus a fresh, new look for the exterior.

“Since its introduction in 2009, the second-generation Kia Sorento has achieved more than 34,000 sales across Europe, following global sales of almost 900,000 units achieved by the original Sorento from 2002.  This all-new model was a ‘landmark’ vehicle in the history of our brand, starting the process of changing public perceptions of Kia as a maker of supposedly only small cars,” commented Benny Oeyen, Vice President Marketing and Product Planning, Kia Motors Europe.

“During the last decade, Sorento has earned widespread public acclaim and attracted thousands of new customers to Kia.  While creating the upgraded Sorento, Kia’s design and engineering teams have paid very careful attention to owners’ feedback, and the result is a new Kia model which is not just a cosmetic exercise but represents a major step forwards for our popular SUV,” added Mr Oeyen.

Introducing a fresh new look with premium appeal

To give the upgraded Sorento a fresh look that reflected the new model’s stronger structure, premium quality and enhanced specification, Kia’s design team restyled the upgraded vehicle’s front and rear, creating larger areas of body-colour surface.  Careful attention to surface detailing cut aerodynamic drag to Cd 0.34.

Kia’s designers developed new front and rear bumpers with unconventional upright fog lights, a new front grille and headlamps with LED positioning lights, and a new tailgate with reshaped LED combination lamps.  Depending on model, the Sorento’s updated styling can be completed with 17-inch, 18-inch or new, optional 19-inch alloy wheels.

A new two-part glass panoramic sunroof with a single powered roller-blind shade will be available.  Seven new exterior colours will be introduced.

New high-tech features and top quality cabin trim

Inside the upgraded Sorento’s cabin, numerous enhancements create a refreshed ambience, with premium high-tech equipment available on some models and an extended choice of options.  The interior can be trimmed in black or beige cloth, or in optional black, beige, brown or black-and-white leather.

Inside the seven-seater cabin, there are more soft-touch surfaces – with a satin chrome finish for the door handles, air-vent surrounds and switches – plus a new LCD instrument cluster, new centre stack with 7-inch LCD display screen and a new centre console featuring (on automatic transmission models), a straight-gate selector with a leather-booted lever – reinforcing the vehicle’s more luxurious character.

Further premium options include powered, heated and ventilated front seats, heated second-row seat cushions, a Bluetooth® hands-free system, UV-reflecting Solar glass, and independent air-conditioning for the third-row seats.

Customers will be also able to specify radar-based BSD (blind spot detection), LDWS (lane departure warning system) using a camera above the windshield and SPAS (smart parking assist system) with ultrasonic sensors to control automatic parallel parking.

Access to the cabin is improved by the lower ride height (down by 10 mm), and the cabin floor has also been lowered, increasing legroom by 30 mm (second row) and 9 mm (third row).

Kia’s engineers have implemented a host of measures to reduce NVH (noise, vibration and harshness) to ensure that the upgraded Sorento boasts even greater refinement than the previous model, making it one of the quietest vehicles in its class.

Enhanced powertrains cut consumption and emissions

Depending on individual market preferences, Kia’s upgraded Sorento will be available with one gasoline and two diesel engines (generating from 150 to 197 ps).  Anticipating consumer trends, Kia has fine-tuned the all-new 2.4-litre GDI gasoline (appearing in a Kia vehicle for the first time in Europe) and the 2.2-litre TCI diesel engine, which are expected to be the most popular customer choices in Europe, to improve their efficiency.

The revised 2.4-litre ‘Theta II’ GDI engine is fitted with a new cylinder head, pistons, fuel injection and intake systems.  It generates 9% more power (192 ps) and 6.6% more torque (242 Nm) – than the 2.4 MPI engine available in some markets outside Western Europe – while delivering better fuel economy (up 14%) and lower emissions, from 199 g/km.

The ‘R’ family of Kia diesel engines has become immensely popular in a variety of Kia models around the world.  In the upgraded Sorento, the 2.2-litre, 197 ps TCI (turbo charged inter-cooler) engine features a new exhaust gas recirculation (EGR) system which reduces CO2 emissions by 14% – down to as little as 153 g/km.  Maximum torque is 436 Nm (automatic models) and 421 Nm (manual).

The smaller capacity 2.0-litre TCI engine generating 150 ps and 382 Nm will also be available.

Six-speed gearboxes, plus choice of 2WD or 4WD

Every upgraded Sorento model will feature a manual or automatic six-speed transmission carried over from the previous model.  Also carried over is the choice of 2WD (front-wheel drive) or 4WD (four-wheel drive) – depending on model.  The 2WD drivetrain offers a weight saving of approximately 60 kg, further enhancing fuel economy.

The 4WD drivetrain is an ‘on demand’ system that delivers 100% of engine torque to the front wheels during all routine city and highway driving.  Whenever a front wheel loses grip a percentage of torque (up to 50%) is automatically transferred to the rear wheels.  In severely slippery conditions the driver can select ‘Lock Mode’ which delivers 50% of torque to both the front and rear axles.

Improved on-road performance, retained off-road capability

Kia chassis engineers worked hard to ensure that while the upgraded Sorento gives rewarding responses to driver inputs, it also delivers a sophisticated ride/handling balance to rival the best vehicles in its class.

While the basic specification of the suspension is unchanged – front MacPherson struts and a multi-link set up at the rear – the subframes which support the suspension are completely new, stronger designs.  They give more precise location of the suspension components and have revised mounting bushes to dampen vibrations.  Larger suspension bushes, longer trailing arms at the rear and HPD (High Performance Dampers) work together to improve ride comfort and stability.

For precise vehicle control and good ‘feel’ the upgraded Sorento’s steering is now more direct, with 2.95 turns of the wheel lock-to-lock.  Kia’s new FlexSteer™ system is an option, providing Normal, Sport and Comfort modes with three different weights to match customer preference.

5-Star standards with advanced ‘active’ and ‘passive’ systems

When it was introduced in 2009, the second-generation Sorento was awarded a 5-Star Euro NCAP safety rating.  Today, official crash test standards in Europe are much tougher and Kia engineers re-visited the upgraded Sorento’s structure and safety equipment to ensure that the new model will also win the accolade of a top safety score in Europe’s Euro NCAP and the USA’s official NHTSA crash tests.

Extensive revisions to the bodyshell, which already incorporates a higher percentage (70.4%) of high-tensile strength steel than most vehicles in its class, have improved front, side and rear impact protection.  Hot stamping is used to heat steel to 900º C and press immensely strong components for the front bumper, centre floor member and rear floor side members – improving crashworthiness.

A bracing bar between the top of the front suspension towers is fitted and the bodyshell’s torsional rigidity has been raised by 18%, enhancing refinement and creating a stronger foundation for the suspension and steering, which benefits ride comfort and directional stability.

Inside, the upgraded Sorento can be equipped with up to six front, side and curtain airbags, while for maximum stopping power, all upgraded Sorento models are equipped with larger diameter (320 mm) ventilated front disc brakes.

All upgraded Sorentos will be fitted with an AHS (active hood system) which raises the trailing edge of the hood during a collision to reduce the severity of pedestrian injury.

Active safety technologies that upgraded Sorento buyers can specify will include ESC (electronic stability control), VSM (vehicle stability management), a KRSC (Kia reversing safety camera) mounted on the tailgate with a 130 degree wide-angle lens, HID (high intensity discharge) Xenon headlamps and HAC (hill-start assist control), which prevents slip-back during stop-start driving on inclines.

Ends

Editors’ Notes

Upgraded Sorento range

Some markets may select particular powertrains and levels of equipment to suit the preferences of their local consumers.  Please check the final technical specification and model equipment details with your national Kia PR representative.

TECHNICAL SPECIFICATIONS / EUROPE

Upgraded Kia Sorento

Body & Chassis

Five-door, seven seater, mid-size SUV with all-steel unitary construction bodyshell.  Choice of transversely mounted gasoline or diesel engines with 2WD (front-wheel drive) or 4WD (four-wheel drive) and six-speed manual or automatic transmission (depending on model and market).

Engines

Gasoline

2.4-litre 192 ps GDI

Type / capacity 	Theta II GDI, 4-in-line, twin DOHC, dual CVVT and VIS / 2359 cc

Power / torque 	192 ps (141 kW) @ 6300 rpm / 242 Nm (24.7 kg.m) @ 4250 rpm

Bore x stroke (mm)	 88.0 x 97.0

Compression ratio 	11.3

Diesel

2.2-litre 197 ps TCI

Type / capacity 	‘R’ 2.2 TCI, 4-in-line, twin DOHC, dual CVVT and VGT / 2199 cc

Power / torque 	197 ps (145 kW) @ 3800 rpm / 421 Nm (43.0 kg.m) @ 1800-2500 rpm

436 Nm (44.5 kg.m) @ 1800-2500 rpm  (automatic)

Bore x stroke (mm)	85.4 x 96.0

Compression ratio 	16.0

2.0-litre 150 ps TCI

Type / capacity 	‘R’ 2.0 TCI, 4-in-line, twin DOHC, dual CVVT and VGT / 1995 cc

Power / torque 	150 ps (110 kW) @ 4000 rpm / 382 Nm (39.0 kg.m) @ 1800-2500 rpm

Bore x stroke (mm)	84.0 x 90.0

Compression ratio 	16.5

Transmissions / drivetrains

2.4 GDI	2.2 TCI 	2.0 TCI

Manual 		6-sp 		6-sp 		6-sp

Automatic 		6-sp 		6-sp 		-----

2WD 			2WD 		2WD 		2WD

4WD 			4WD 		4WD 		4WD

Drivetrains

Type 			2WD (front-wheel drive)

Type 			4WD (four-wheel drive)

Operation 	Normal driving, front-wheel drive only.  If the ‘on demand’ system detects front wheel ‘slip’ a percentage of engine torque is transferred to the rear wheels, up to 50/50% front/rear torque split.  To maximize traction, system can be locked in 50/50% torque split up to 40 kph.

TECHNICAL SPECIFICATIONS / Upgraded Kia Sorento

Suspension and damping

Front   	Fully independent by subframe-mounted MacPherson struts, with coil springs and gas-filled HPD shock absorbers and anti-roll bar.

Rear 	Fully independent by subframe-mounted multi-links, with coil springs and gas-filled HPD shock absorbers and anti-roll bar.

Steering

Type 			MDPS electric power-assisted rack & pinion with FlexSteer™ option

Gearing 		2.95 turns lock-to-lock

Turning circle 		10.9 meters

Brakes

Power			Single 10.5-inch Booster

Front / Rear  		320 x 28 mm ventilated discs / 302 x 11 mm solid discs

Assistance		ABS anti-lock with EBD and BAS

100-to-0 kph 		36.3 / 37.0 metres  (cold / warm modes)

Wheels and tyres

Standard 		Alloy 17 in x 7.0J	235/65 R17

Optional 		Alloy 18 in x 7.5J	235/60 R18*

Alloy 19 in x 8.0J 	235/55 R19*

Temporary Spare 	Mobility Kit 		*depending on model

DIMENSIONS (mm)

Exterior

Overall length		4685

Overall width		1885*

Overall height		1700 		1735 (with roof rails)

Wheelbase 		2700

Front overhang	  945

Rear overhang	1040

Front track** 		1623-1626

Rear track** 		1618-1621

Ground clearance 	  185

Approach angle 	19.4 deg

Departure angle 	22.1 deg

Ramp over angle 	16.6 deg

Aerodynamics 	0.34 Cd

*excluding door mirrors, **depending on wheel/tyre combination

Interior			Front 		2nd Row	3rd Row

Headroom 		  996 		  995 		  906

Legroom		1048 		  985 		  804

Shoulder room 	1506 	 	1491 		1045

Hip room		1431 		1421 		1128

Capacities

Fuel tank (litres)	70.0

Luggage (SAE) 	258 litres 	(behind 3rd row) to roof

1047 litres 	(behind 2nd row) to roof

2052 litres 	(behind front seats) to roof

TECHNICAL SPECIFICATIONS / Upgraded Kia Sorento

Manual models

2WD

Weights (kg) 		2.4 GDI 	2.2 D 		2.0 D

Curb (minimum)	1605  		1720 		1720

Gross (maximum) 	2510  		2510  		2510

Towing (braked) 	2000  		2000 		2000

Performance*

Top speed / kph 	190 		190 		187

0-to-100 kph / sec 	9.8 		9.3  		10.8

Economy**

Litres / 100 km	8.7  		5.8 		6.1

CO2 g/km 	 	202 		153 		159

4WD

Weights (kg) 		2.4 GDI 	2.2 D 		2.0 D

Curb (minimum)	1675  		1787 		1787

Gross (maximum) 	2510  		2510 		2510

Towing (braked) 	2000 		2000 		2000

Performance*

Top speed / kph 	190 		190 		186

0-to-100 kph / sec 	10.3 		9.7 		11.1

Economy**

Litres / 100 km	8.9 		5.9 		6.1

CO2 g/km 	 	207 		155 		160

Automatic models

2WD

Weights (kg) 		2.4 GDI 	2.2 D 		2.0 D

Curb (minimum)	1605 		1748 		-----

Gross (maximum) 	2510  		2510 		-----

Towing (braked) 	2000 		2000 		-----

Performance*

Top speed / kph 	190 		190 		-----

0-to-100 kph / sec 	10.2 		9.7 		-----

Economy**

Litres / 100 km	8.6  		6.4 		-----

CO2 g/km 	 	199 		169 		-----

4WD

Weights (kg) 		2.4 GDI 	2.2 D 		2.0 D

Curb (minimum)	1698 		1815 		-----

Gross (maximum) 	2510  		2510 		-----

Towing (braked) 	2000 		2000		-----

Performance*

Top speed / kph 	190 		190 		-----

0-to-100 kph / sec 	10.7 		9.9 		-----

Economy**

Litres / 100 km	8.9 		6.7 		-----

CO2 g/km 	 	208 		175 		-----

*Figures stated are manufacturer’s estimates, **Combined cycle, cars with 17-inch wheels

SEPTEMBER 2012