9.  TECHNICAL SPECIFICATIONS / EUROPE

New Kia Sportage

Body & Chassis

Five-door, five-seater compact SUV, with all-steel unitary construction bodyshell.

Choice of four transversely-mounted diesel and gasoline engines driving the front (2WD) or front and rear wheels (AWD) via a five-speed or six-speed manual or six-speed automatic transmission – depending on model.

Engines

DIESEL

2.0-litre / 136 ps Diesel  [ Available from launch ]

Name / Type 		‘R2.0’ / DOHC, four-cylinder in line, with single VGT

Capacity 		2.0-litres, 1995 cc

Max power 		136 ps (100.0 kW) @ 4000 rpm

Max torque 		319 Nm (32.6 kg.m) @ 1800-2500 rpm

Fuel system 		CRDi, common-rail, high pressure, direct injection

Turbo system 		Variable geometry turbocharger (VGT)

Emissions class 	Euro 5

1.7-litre / 115 ps Diesel  [ Available from late 2010 ]

Name / Type 		‘U2’ / DOHC, four-cylinder in line, with single VGT

Capacity 		1.7-litres, 1685 cc

Max power 		115 ps (84.5 kW) @ 4000 rpm

Max torque 		255 Nm (26.0 kg.m) @ 1800-2500 rpm

Fuel system 		CRDi, common-rail, high pressure, direct injection

Turbo system 		Variable geometry turbocharger (VGT)

Emissions class 	Euro 5

GASOLINE

2.0-litre / 163 ps Gasoline  [ Available from launch ]

Name / Type 		‘Theta II’ / DOHC, four-cylinder in line, with dual CVVT

Capacity 		2.0-litres, 1998 cc

Max power 		163 ps (120.0 kW) @ 6200 rpm

Max torque 		195 Nm (19.8 kg.m) @ 4600 rpm

Fuel system 		Multi-point injection

Emissions class 	Euro 5

1.6-litre / 140 ps Gasoline  [ Available from late 2010 ]

Name / Type 		‘Gamma’ / DOHC, four-cylinder in line, with dual CVVT

Capacity 		1.6-litres, 1591 cc

Max power 		140 ps (103.0 kW) @ 6200 rpm

Max torque 		166 Nm (17.0 kg.m) @ 4500 rpm

Fuel system 		Multi-point injection

Emissions class 	Euro 5

Transmissions

2.0D 		1.7D		2.0G 		1.6G

Manual  		6-sp  		6-sp 		5-sp 		6-sp

Automatic  		6-sp 		---- 		6-sp 		----

Drivetrains

2.0D MT/AT	1.7D MT 	2.0G MT/AT 	1.6G MT

2WD 			S / ---- 		S		S / S 		S

AWD 	  		S / S 		----		S / S 	----

S = available as standard

2WD

Delivers 100% of torque/power to the front wheels.  Safety aided by electronic Traction Control, ABS anti-lock braking and (optional for some countries) ESC with Downhill Brake Control and Hill-start Assist Control.

AWD

Permanent electronically controlled AWD system with single ratio (High).  Delivers 100% of torque to front wheels during normal road driving and up to 60/40 (front/rear) split depending on conditions.  Manually selected ‘Lock Mode’ splits torque 50/50 between front/rear axles for enhanced stability during slippery conditions (up to 40 km/h).

Suspension & Damping

Front 	Fully independent by subframe-mounted MacPherson Struts, with coil springs and gas-filled shock absorbers. Anti-roll stabiliser bar.

Rear 	Fully independent by subframe-mounted multi-links, coil springs and gas-filled shock absorbers.

Steering

Type 			MDPS, electric power-assisted rack and pinion

Overall ratio 		15.9:1

Gearing 		2.96 turns lock-to-lock

Turning circle 		10.58 metres

Brakes

Power 			Single 11 -inch booster (LHD)

Tandem 8- & 9-inch booster (RHD)

Front 	  		300 x 28 mm ventilated discs

Rear			262 x 10 mm solid discs (2WD)

284 x 10 mm solid discs (AWD)

Parking brake 		Hand operated lever

ABS 			4-channel anti-lock system with EBD

BAS			Boosts braking power during emergency stops

DBC 			Downhill brake control maintains 8 km/h speed during descents

Wheels & Tyres

Standard  		Alloy 16 in x 6.5J		215/70 R16 tyres

Options 		Alloy 17 in x 6.5J 		225/60 R17 tyres

Alloy 18 in x 6.5J 		235/55 R18 tyres

Spare (Standard) 	Tyre mobility kit

Spare (Option) 		Full size alloy wheel and tyre

DIMENSIONS (mm)

Exterior

Overall length 		4440 		Overall width* 		1855

Overall height 		1635** 		Wheelbase 		2640

Front track 		1614 		Rear track 		1615

Front overhang		 890 		Rear overhang 		 910

Ground clearance 	 172

*excluding door mirrors / **excluding roof rack

Interior 			Front 		Rear

Headroom 		 992 		 977

Legroom 		1051 		 963

Shoulder room 		1440 		1400

Hip room		1364 		1246

Capacities  		(all models)

Fuel tank 		58 litres

Luggage (VDA) 	564 litres (behind rear seats

1353 litres (behind front seats, rear seats folded

Off-road Capabilities

Approach angle 	22.7 degrees 		Departure angle 	28.2 degrees

Ramp over angle	17.7 degrees 		Roll over angle 		45.0 degrees

Max climb angle 	44.2 degrees

Weights (kg)

2.0D MT/AT	1.7D MT 	2.0G MT/AT 	1.6G MT

All-wheel drive

Kerb weight (min.)	1600/1676	---- 		1525/1544 	----

Gross weight 		2140/2140			2030/2030

2-wheel drive

Kerb weight (min.)	1533/-  	x		1455/1472	x

Gross weight 		2090/- 		x		1980/1980	x

Performance

2.0D MT/AT	1.7D MT 	2.0G MT/AT 	1.6G MT

All-wheel drive

Top speed / kph 	181/181		---- 		182/180		----

0-to-100 kph / sec 	11.3/12.1			10.7/11.2

Towing (max) kg* 	2000/1600			1900/1600

2-wheel drive

Top speed / kph 	182/- 		x		184/182		x

0-to-100 kph / sec 	10.8/-				10.4/10.6

Towing (max) kg* 	2000/-	 			1900/1600

*trailer with brakes

Fuel Economy (litres/100 km)*

2.0D MT/AT	1.7D MT 	2.0G MT/AT 	1.6G MT

All-wheel drive

Combined cycle 	5.7/6.9		X 		7.6/8.2		X

CO2 g/km		149/179		---- 		181/195		----

2-wheel drive

Combined cycle 	5.5/- 		X		7.5/7.9		X

CO2 g/km 		147/-		---- 		177/187 	----

*fuel consumption and CO2 data, manufacture’s estimated figures

JUNE 2010