Embargoed: Not to be published before 11.30 CET, 4 March 2014

Kia previews future powertrain technologies with all-new mild hybrid system

- New mild hybrid powertrain combines zero-emissions urban motoring with an electric supercharger for greater performance

- Engineered to reduce diesel and gasoline emissions by up to 15 percent

- New powertrain will be available on next-generation Kia models

Geneva, 4 March 2014 – Kia revealed its all-new mild hybrid powertrain today at the Geneva Motor Show. The powertrain – part of a future technologies exhibit on Kia’s show stand – is designed to simultaneously reduce emissions and improve engine performance in Kia’s next-generation models.

Developed by Kia’s European R&D centre, the new hybrid system employs a 48V lead-carbon battery, which powers a small electric motor to increase the engine’s power output and cut exhaust emissions. The development team behind the mild hybrid powertrain selected lead-carbon batteries over lithium-ion equivalents as they require no active cooling, are more easily recyclable at the end of the vehicle’s life and can function much more efficiently in sub-zero temperatures.

Kia’s mild hybrid system will enable a car to be driven in an electric-only mode at low speeds and when cruising, while the battery is recharged under deceleration at all speeds. In heavy traffic and on urban roads, the powertrain will also feature a zero-emissions stop-start system. Using a belt-driven starter generator – replacing the conventional alternator – the engine is able to restart with almost no noise or vibration.

The battery also supplies energy to an electric supercharger, which increases torque and power at low engine speeds. Engineers behind the development of the powertrain see the electric supercharger supporting a larger conventional turbocharger, which would seamlessly take over to provide greater power and torque as engine speeds rise. The new hybrid system could also be fitted without the electric supercharger for a simpler powertrain layout in smaller models.

In applying the technology to production cars, Kia engineers are targeting reductions in CO2 emissions of up to 15 percent, while the electric supercharger is designed to deliver power increases of 15 to 20 percent depending on its application.

The new powertrain would also allow vehicle development engineers to reduce the size of a vehicle’s existing battery and starter motor.

The new mild hybrid powertrain will be available on new diesel and gasoline production cars from Kia in the near future.

- Ends -

Editors’ Notes

Kia Motors Europe

Kia Motors Europe is the European sales, marketing, and service arm of Kia Motors Corporation. With its headquarters in Frankfurt, Germany, it covers 30 markets in Europe.

# About Kia Motors Corporation

Kia Motors Corporation (www.kia.com) – a maker of quality vehicles for the young-at-heart – was founded in 1944 and is Korea's oldest manufacturer of motor vehicles. Over 2.7 million Kia vehicles a year are produced in 10 manufacturing and assembly operations in five countries which are then sold and serviced through a network of distributors and dealers covering around 150 countries.

Kia today has over 48,000 employees worldwide and annual revenues of US$43 billion. It is the major sponsor of the Australian Open and an official automotive partner of FIFA – the governing body of the FIFA World Cup™. Kia Motors Corporation's brand slogan – "The Power to Surprise" – represents the company's global commitment to surprise the world by providing exciting and inspiring experiences that go beyond expectations.